## Slide 1
Reactive Navigation in Crowds for Non-holonomic Robots with Convex Bounding Shape
20233201 JIHYEOK KIM
CS686 Paper Presentation I
IEEE ROBOTICS AND AUTOMATION LETTERS 2021

## Slide 2
TerraPN: Unstructured Terrain Navigation using Online Self-Supervised Learning
REVIEW
1
Improve navigability cost using non-uniform sample patches
Compute collision free trajectories with Dynamic Window Approach

## Slide 3
BACKGROUND
Robot navigation in crowded environment
need to coordinate with pedestrian
should predict their intentions and avoid collision safely

## Slide 4
BACKGROUND
Velocity Obstacle
velocity based approach to avoid collisions with moving obstacles
Velocity obstacle
Collision-avoidance velocity
Minkowski Sum

## Slide 5
RELATED WORK
Optimal Reciprocal Collision Avoidance (ORCA)
Assume circular holonomic agents
Reduce the capability for non-holonomic agents to plan through narrow passage

## Slide 6
METHODS
Reactive Driving Support (RDS)
Using capsule model to describe the robot’s shape
Model accounts for non-holonomic kinematics preventing sideways motions
Optimization Problem

## Slide 7
Simulation Framework
Robot and pedestrians follows the reference trajectory
Pedestrians avoid each other and the robot by ORCA
Robot uses RDS or ORCA
pedestrians
Reference trajectory:
Robot (RDS)
Robot (ORCA)
EXPERIMENT:
Simulation

## Slide 8
EXPERIMENT:
Simulation
The robot’s mean tracking error
The crowd’s velocity reduction due to the robot
The neighbors-to-crowd velocity (3m)
Collision with robots
Performance Metrics

## Slide 9
EXPERIMENT:
Simulation I
Crossing with Variable Head Start
Speed: 1.3 m/s

## Slide 10
EXPERIMENT:
Simulation II
Navigating in a Sparse Crowd
RDS
Baseline
The robot’s mean tracking error
The crowd’s velocity reduction due to the robot
The neighbors-to-crowd velocity (3m)
Collision with robots

## Slide 11
EXPERIMENT:
Real Robot
Qolo: Electrically powered standing wheelchair
1) SLAM:
- LiDAR SLAM (hector slam)
2) Person Detection & Tracking:
- LiDAR + RGBD Cam
3) Collision Avoidance:
- Reactive Driving Support

## Slide 12
EXPERIMENT:
Real Robot I, II
Test in Static Environment: Door
RDS
Baseline
Test with Pedestrians
RDS
Baseline

## Slide 13
EXPERIMENT:
Real Robot II
Test with Pedestrians: Video

## Slide 14
CONCLUSION
Developed a method to apply the Velocity Obstacle to non-holonomic capsule-shaped robots
More advantageous in crowds due to its ability to lead through narrow gaps
Successfully avoid static or dynamic obstacles in both simulation and real world

## Slide 15
QUIZ
Q1) This paper developed a method to apply the VO to non-holonomic capsule-shaped robots. What is VO?
a) Visual Odometry b) Value Object c) Virtual Override d) Velocity Obstacle
Q2) Which one is True about Reactive Driving Support (RDS)?
Using circular model to describe the robot’s shape
Model accounts for non-holonomic kinematics preventing sideways motions

## Slide 16
THANK YOU
Thank You